cONTRIBUTION:	XXXX	 2003 02 11

working Group:	Network Working Group

title:	test results from remote dslam installation

Issues Addressed:	This contribution reports the measurements TELUS captured on a test circuit when DSL subscribers were cut onto a DSLAM remote.

Source:	Telus Corporation
Ed Ng	Marc LaBelle	Craig Miller

Floor 18G,	Floor 24	Floor 18 E

10020–100 St.	10020-100 St.	10020-100 St.
Edmonton, AB	Edmonton, AB	Edmonton, AB

780 493-5128	780 493-2523	780 493-5448

Distribution:	NTWG Interested Parties

REFERENCE:

FILE NAME:

Notice:	This contribution has been prepared by TELUS Communication Inc. to assist the Network Working Group as basis for discussion. This should not be construed as a binding proposal on TELUS Communications Inc. Specifically, TELUS Communications Inc. reserves the right to request amendments, modifications or to withdraw of this contribution at any time.

# INTRODUCTION

Several months ago TELUS volunteered to provide the NTWG data to be collected from field tests being planned to measure the interference on CO fed DSL customers when other DSL customers within the same binder group were fed from a remote DLSAM.  This contribution provides these results.

TELUS recognizes that the amount of data provided in this contribution is not statistically significant but it does represent 100% of the instances where this configuration was implemented in TELUS’ Alberta region from the time the offer was made to the present time.

# TEST DISCRIPTION

In NTCO210 TELUS documented the following test plan.  It is reiterated below:

It is assumed that CO served circuits will suffer more crosstalk interference when both CO ASDL circuits and remote ADSL circuits appear in the same binder group.  Based on this assumption, TELUS will select two copper pairs from the CO served feeder and distribution cables as the victim circuits, perform metallic loop tests and make any necessary corrective repair to ensure they are free of any foreign voltages, grounding, etc.  Once the victim pairs are accepted, TELUS will connect them to the ADSL ports in the CO and perform the following tests to be used as a reference parameter.

- Modem Train-up Rate (Downstream and Upstream)

- Data Throughput (Upstream and Downstream)

- Power Spectrum Density Measurement (PSD)

Once these reference parameters are established, all the existing TELUS ADSL circuits will be cut from the feeder cables to the remote DSLAM one at a time.  The same spectral interference tests will be performed after each cutover until all the circuits are reassigned.  The results will then be documented and compared to the reference results.

# Test Configuration

TELUS plans to conduct these spectral interference field measurements in seven locations, six where remote DSLAMs are being installed and one where an ADSL capable Digital Loop Carrier system is being established. All of these systems are fiber fed from the central office.  The length of copper feeder cable between the CO and the JWI/OPI ranges from approximately 3 km to 4.5km (reference section A in Figure 1 and column 2 of Table 1).  The wire gauge of the feeder cables is 26AWG or 24AWG or a combination of both as shown in Table 1.  The distribution copper cable from the JWI/OPI to the customer premises is 1.5 km or less (section B).  The distance between the remote DSLAM and the JWI/OPI is no more than 200 meters, and the distance between the DLC and the JWI/OPI is approximately 400 meters (section C).

Figure 1. Test Configuration

TELUS did not perform tests at the 7 test locations indicated above for a variety of reasons but did carry out tests at two locations in Edmonton.   Figures 2 and 3 illustrate the actual test configuration.

###### Figure 2. NW Edmonton Test Configuration

###### Figure 3. SW Edmonton Test Configuration

TEST RESULTS

The two tests were both conducted in the Edmonton exchange, one in NW Edmonton and the other in SW Edmonton.

NW Edmonton

The NW Edmonton tests did not encompass a full range of data rate measurements due to time, personnel and scheduling constraints.  Instead, a simple “go/no go” test was conducted.  This was done in the following manner.  First the test circuit was powered down, next a disturber circuit from the test circuit’s binder group was added to the remote DSLAM, then the test circuit was powered up.  If the test circuit operated, it was recorded as a “go”.  If it didn’t, it was classified as a “no go”.

These tests showed that the test circuits trained up after the first five disturbers were added to the remote DSLAM but failed on the sixth.  To verify the result the test circuit was powered down and the sixth circuit removed from the remote DSLAM.  The test circuit was then powered up and it worked.  Down stream and up stream data rates were then recorded.  The data rate tests showed the down stream rate to be 896 kbps and the up stream rate 640 kbps.

SW Edmonton

The SW Edmonton tests did not have the same constraints as the NW Edmonton tests so both up stream and down stream data rates were measured after each disturber circuit was added to the remote DSLAM.   These measurements are captured in Table 1 and illustrated in Graph 1.

| Number of Disturbers | Down stream Data Rates (kbps) | Up Stream Data Rates (kbps) |
| --- | --- | --- |
| 0 | 4096 | 800 |
| 1 | 3680 | 864 |
| 2 | 3744 | 832 |
| 3 | 3360 | 864 |
| 4 | 3232 | 844 |
| 5 | 3168 | 864 |
| 6 | 2944 | 768 |
| 7 | 2880 | 864 |
| 8 | 2432 | 736 |
| 9 | 2336 | 800 |
| 10 | 2208 | 832 |
| 11 | 2112 | 832 |
| 12 | 2080 | 832 |
| 13 | 1888 | 800 |
| 14 | 2048 | 800 |
| 15 | 1856 | 832 |
| 16 | 1760 | 800 |
| 17 | 1760 | 800 |
| 18 | 1632 | 800 |
| 19 | 1536 | 800 |
| 20 | 1504 | 800 |
| 21 | 1440 | 800 |

Table 1. SW Edmonton Test Results

Graph 1. SW Edmonton Test Results

These results show a constant deterioration of the down stream rates as more disturbers were added to the remote DSLAM.

CONCLUSION

The tests performed in the field are limited and are not statistically significant but do indicate that down stream data rates decrease on CO based ADSL circuits when adjacent ADSL circuits (i.e. circuits in the same binder group) are added to a remote DSLAM.  These finding are consistent with ANSI-T1’s theories and Bell Canada’s lab tests.